## Slide 1
ARGUS: Adaptive Real-time Guardian for Unified Surveillance
Guide: Prof. Vivek Shripad Nagnath | Arya Petkar (1251030275), Shatakshi Petkar (1251030199), Swayam Phadtare (1251030068),
Suyash Sawant, Ritik
Department of Engineering Science and Humanities (DESH)
Vishwakarma Institute of Technology, Pune
ASE PROJECT 2 ASSESSMENT JUNE 2026
Introduction
ARGUS is an AI-powered offline exam malpractice detection system using MediaPipe Pose estimation, motion analysis, and a Random Forest ML classifier to monitor student behaviour in real-time exam halls.
The system extracts 7 behavioural features per student per frame and builds a cumulative suspicion score per bench zone. A confirmed alert fires only after 7 seconds of sustained suspicious behaviour, eliminating false positives from brief movements.
A physical Arduino console with Green/Amber/Red LEDs, active buzzer, and I2C LCD provides graduated real-time alerts. Every session auto-generates a PDF and Excel report with full incident log, bench assignments, ML confidence, and timestamps.
ABSTRACT
METHODOLOGY
RESULTS AND DISCUSSIONS
The system
The system.
The system
preventing long waiting times and congestion.
The system
ata security, which should be addressed through proper regulations and protocols.
Stretch posture (arm reach) correctly classified as non-cheating (label=0) after v3 ML retraining, eliminating the most common false-alert source.
FLOW CHART
TESTING / IMPLEMENTATION
NOVELTY FEATURES / FINDINGS
Cumulative Suspicion Scoring — score builds over sustained behaviour, not single-frame spikes; eliminates false positives from brief glances or stretches.
Stretch modeled as label=0 in ML training (v3) — system correctly ignores normal arm reaches; trained on real 2-3m camera-distance measurements.
Three-tier hardware severity (Green/Amber/Red LED) — screen-independent alert system; invigilator informed even while walking the hall.
ArUco auto-calibration — bench zones mapped in ~10 seconds; no manual coordinate entry required for any exam hall layout.
Fully offline architecture — no cloud, no internet, no privacy risk; suitable for secure VIT exam hall deployment.
Excel seating upload — official VIT seating Excel directly maps student PRNs to detection zones; zero manual entry.
Oooo
7-second sustained detection threshold — realistic for actual cheating; prevents false alerts from momentary suspicious movements.
Alert persistence (30s) — red LED stays on and dashboard alert persists for 30 seconds even if student returns to normal posture.
Dataset: 4,500 synthetic samples generated using real 2-3m camera-distance measurements (normal: 1,500, stretch: 1,500, cheating: 1,500). Features: shoulder_angle, head_offset_x/y, wrist distances, wrist_velocity_avg, zone_motion_score.
Setup: Python 3.11, OpenCV-contrib, MediaPipe, scikit-learn, Flask, PySerial, ReportLab, openpyxl. Arduino IDE with LiquidCrystal_I2C library. Run: py -3.11 webapp/app.py → open localhost:5000.
Hardware test: Arduino sketch v4 uploaded; boot LED sweep (Green→Amber→Red) verified; 3-LED single-mode, buzzer, and I2C LCD all confirmed functional on COM5.
ArUco calibration: Printed 10x10 cm markers (IDs 0,1,2) placed at 2-3m; Scan ArUco button auto-saved zones.json with correct bench coordinates in ~10 seconds.
Full 3-student test: Arya (B1), Shatakshi (B2), Swayam (B3) seated at 2-3m. Normal posture — no alert. Cheating posture held 7+ seconds — amber LED → red LED + 3 beeps + LCD + toast notification. Stop Exam → Excel auto-downloaded + PDF saved.
CONCLUSIONS
ARGUS successfully demonstrates AI-powered offline exam malpractice detection — all 12 core modules built, tested, and integrated into a single cohesive system.
The 7-second sustained detection and stretch-as-normal ML training effectively balance sensitivity and specificity, making the system practical for real exam scenarios.
Hardware-backed graduated alerts (Green/Amber/Red) provide screen-independent, real-time severity indication suitable for active exam hall invigilation.
Auto-generated PDF and Excel reports provide complete, tamper-evident, evidence-backed documentation for disciplinary proceedings at VIT Pune.
ArUco zone calibration and Excel seating integration make deployment practical for any exam room without manual configuration.
The fully offline architecture ensures privacy compliance and internet-independence, meeting the requirements of secure examination environments.
Oooo
The system has been validated end-to-end in a 3-student demo; hardware, detection, dashboard, and reporting all confirmed functional and demo-ready for June 2026 review.
ASEP 2
GROUP NO.
CSAIML-E Gr.01
INTRODUCTION
Exam malpractice in offline pen-paper exams remains a major challenge in Indian universities. Invigilators cannot monitor all students simultaneously, and no standardised AI-based offline detection system exists.
Traditional manual invigilation is subjective and error-prone. Students exploit brief moments of invigilator inattention to copy, pass chits, or look at neighbours — behaviours lasting 5-10 seconds.
ARGUS addresses this gap using a single webcam, MediaPipe Pose (33 body landmarks), motion zone analysis, and Random Forest ML classification to create an automated evidence-based pipeline.
The system operates fully offline with no internet dependency — critical for deployment in secure VIT exam halls where network access is restricted or unavailable.
All alerts produce hardware-backed responses (LED + buzzer + LCD) and generate tamper-evident audit trails — suitable for official disciplinary proceedings as per VIT academic regulations.
The project was developed by Group 01, CSAIML-E, VIT Pune, under the guidance of Prof. Vivek Shripad Nagnath, as part of the Applied Science and Engineering Project (ASEP) 2025-26.
IMP 2/3 IMAGES OF PROJECT
IMAGE 1
IMAGE 2
BLOCK DIAGRAM
ACTUAL CIRCUIT/ DESIGNED SYSTEM